## SECTION 12 2000

### SPECIFICATION FOR AUTOMATED MOTORIZED SHADES.

Pleated Shade System

- General

  - Section Includes:

    - Stationary Pleated Shade

  - Related sections:

    - Section 06100 Rough Carpentry

    - Section 08520 Aluminum Windows

    - Section 08920 Glazed Aluminum Curtain Wall

  - Summary:

    - Provide stationary pleated interior skylight single solar shade, with related hardware to complete the installation to the following locations:

      - Location of shades – refer to plans

    - Pleated shades shall be mounted between the mullions on the underside of the skylight system. As shown on the plans.

  - Quality Assurance

    - All bidders submitting bids on the work of this section shall meet or exceed the quality of materials, components and assemblies specified herein Bidders who do not comply with these performance specifications shall refrain from submitting a bid.

    - All work specified under this section supplied and installed entirely by one Subcontractor using his own forces.

    - Manufacturer shall have a minimum of twenty (20) years’ experience in the manufacturing of specified shading system.

    - Shades to be installed by a firm, with a minimum of ten (10) years’ experience, specializing in the installation of shading systems.

    - Conform to applicable Building Code and Local Authority having jurisdiction and all other standards noted.

  - Submittals and Test Reports

    - Submit fully detailed drawings prepared in AutoCAD 2002/2004 format showing all components, finishes and perimeter construction conditions, installation, wiring and controls, and all applicable dimensions according to Section 01300 - Submittals.

    - Submit duplicate samples of the specified fabric / shade cloth of each color and texture minimum size 8.5@ x 11@ (215mm x 280mm) for review.

    - Submit duplicate copies of compliance to the following tests

      - Fire tests: Class A/ 1

    - Submit duplicate copies of maintenance instructions including, name and telephone number of local service company.

  - Inspection/ Preparation

    - Verify that all blocking and framing necessary to carry shade assembly hardware is properly installed and secure.

    - Notify Owner in writing of any deficiencies in the work of other trades that would affect the window treatment system.

    - Make accurate measurements at the site before fabrication. Check layout of glazing framing sections, spans, and loading capabilities.

  - Delivery Storage and Handling:

    - Do not deliver to site until areas to receive shades are completely finished, all walls and ceilings completed and painted.

    - Deliver materials in original protective wrappings or containers, with manufacturer’s labels and sealed intact.

    - Handle and store materials according to manufacturer’s recommendations protecting materials and finishes from damages, marring of finishes or soiling.

  - Warranty

    - Provide a limited manufacturers warrantee from the Date of Substantial Completion, covering the following:

      - Shade Hardware: Five (5) years

      - Fabrics / Shade Cloth: Five (5) Years

    - Provide a limited installation warranty from Date of Substantial Completion, covering a period of one (1) year.

- Products

  - Manufacturer:

    - Basis of design: Automated Motorized Shades 3117 NW 25th Ave

    - Pompano Beach, FL 33069

Tel (954) 974-0525; Fax (954) 974-529

E-Mail: info@amsshades.com	, www.amsshades.com

Estimator: Marty Rakitin marty.rakitin@amsshades.com 
(954) 945-0525 x305

  - Hardware:

    - Shade Mounting

      - Mounting shall consist of (1) aluminum tension rod through every hem/ pleat. Hem/ pleats are to occur at every 12” max. per plans.

      - Shades to be fully assembled and tested before delivery to site by manufacturer.

    - Shade Cloth:

Insert desired fabric from “Automated Motorized Shades’s Fabric Specification” below

- Visually Transparent Single-Fabric Shade Cloth:

- Vinyl Room Darkening Single-Fabric Shade Cloth:

- Room Darkening Shade Cloth with Opaque Acrylic Backing:

- Environmentally Certified Shade Cloth

3.0 	Execution:

    - Examination:

      - Do not begin installation until substrates have been property prepared.

      - If substrate preparation is the responsibility of another installer, notify Architect/Contractor of any unsatisfactory preparation before proceeding.

    - Preparation:

      - Contractor shall clean surfaces thoroughly prior to installation.

      - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

    - Installation:

      - Install shades level, plumb, and true according to manufacturer’s written instructions.

END OF SECTION